## Slide 1: Heat Exchanger Selection & Mounting
Hand Calculations & FEA

## Slide 2: Table of Contents
Problem
Costs/Advantages
Coolant Temp
Flowrate
Heat Rejection
Heat Exchanger
System Architecture
Selected Location
Mount FEA

## Slide 3: Problem - Overheating

## Slide 4: Problem - Overheating
This issue is manageable in software (we can add a hysteresis so the torque doesn’t oscillate so much)
The actual temperature limit is different than what Magna originally indicated
  Was 105°C -> Now 130°C
Increasing the flow should completely remove this issue

## Slide 5: Problem – Boost Mode Inoperable
Boost Mode Requirement:
  > 8 L/min
Ideal Nominal Flow:
  10 L/min
System Flow:
  Front: 7.95 L/min
  Rear: 6.60 L/min

## Slide 6: Costs/Advantages
Current System
Cost: $0
Points: -45/1000 (for 0-60 and 50-70 acceleration)
Time: 0
Risk: No boost mode or maximum performance
Modified System
Cost: $1k-3k
Points: +45/1000 (for 0-60 and 50-70 acceleration)
Time:
  60+ hrs design
  30+ hrs manufacturing
Risk:
  Vehicle not ready for CARB
  Motors overheat more

## Slide 7: Coolant Temp
Max Coolant Temp = 46.11 °C
Nominal = 42.6 °C
  Note: Max coolant temp during CARB PCM energy consumption event = 36.5 °C
Max Allowable Coolant Temp = 57 °C
  Magna EDU requirement
This data proves the radiator is sufficient for thermal rejection of system

## Slide 8: Flowrate
Current:
  Front: 7.95 L/min
  Rear: 6.60 L/min
Desired:
  Front: 10 L/min
  Rear: 10 L/min
  Nominal (max)
  20 (25) L/min
  5.28 (6.60) GPM

## Slide 9: Heat Rejection
Maximum
  91,746 BTU/Hr
  26.888 kW
Nominal
  25,796 BTU/Hr
  7.56 kW

## Slide 10: Heat Rejection - Power
Power = Work / Time

## Slide 11: Heat Rejection - Efficiency
Confidential Efficiency Map for the Electric Drive Units

## Slide 12: Heat Rejection - Power Loss
Maximum: 13.444 kW
Average: 3.780 kW
Two Motors:
  Maximum: 26.888 kW
  Average: 7.56 kW
Confidential Power Loss Map for the Electric Drive Units

## Slide 13: Heat Exchanger Selected
Max Pressure: 3100 kPa
Max Temperature: 204 °C
Weight: 6.97 lb
Cost: $ 564.51
Total Area: 0.636 m^2
Pressure Drop: 7 kPa
Max Flow: 62 GPM
CB30-18H - Alfa Laval CB30-18H - 450,000 BTU/Hr (Domestic Water) CB30 Brazed Plate Heat Exchanger (18 Plates)
For more information, see the following slides in this section which cover alternatives and more of the reasoning.

## Slide 14: Heat Exchanger Bell & Gossett
Water - Water
99,900 > 91,746 BTU/Hr
5.4 > 5.28 GPM
Weight: 3.00 lb
Cost: $386.19
Propylene - Water
87,900 ~ 91,746 BTU/Hr
5.41 > 5.28 GPM
Weight: 74.00 lb
Cost: $6357.95
bell-&-gossett-brazed-plate-heat-exchanger-selection-tables.pdf

## Slide 15: Heat Exchanger Wessels
Water - Water
125,000 > 91,746 BTU/Hr
5.2 ~ 5.28 GPM
Weight: 5 lb
Cost: ?
How To: Size Brazed Plate Heat Exchangers | Wessels Company

## Slide 16: Heat Exchanger Wessels
Water - Water
100,000 > 91,746 BTU/Hr
5.0 ~ 5.28 GPM
Weight: 5 lb
Cost: ?
How To: Size Brazed Plate Heat Exchangers | Wessels Company

## Slide 17: Heat Exchanger Alfa Laval
New selection*
Max Heat Transfer
Max Flow Rate
Min Outlet Temperature
Max Inlet Temperature
Max Flow Rate
We now know the stock side should have a flow of 11.3L/min and to assume a nominal input temperature on the cold side of 20°C

## Slide 18: Heat Exchanger Danfoss
Danfoss HEXSelector | Danfoss

## Slide 19: Heat Exchanger Comparison
Heat Exchangers.xlsx
Some HXs stated their max operating values and other stated what was imported into a calculator
Total area x pressure should be proportional to the heat transfer.
As turbulence increases, so does the pressure drop and heat transfer. I expect this means that as pressure drop increases, so does the heat transfer.
1
2
3
Pressure drop: 30 kPa
Pressure drop: 7 kPa
Pressure drop: 20 kPa
** The heat transfer of 26.888 kW is considerable conservative on its own.

## Slide 20: System Architecture: Current
Assumptions:
0% LTR
Temp
  60 ⁰C (GM Parts)
  20 ⁰C (FDU + RDU) this gives us a conservative estimate; as temperature increases pressure decreases
Flow (Ideal)
  20 L/min (system)
  10 L/min (FDU)
  10 L/min (RDU)
RDU
FDU
IPE
Radiator
Split Loop Direction
Pump
Flowmeter
Flowmeter
80 W
∆P = 6.895 kPa
∆P = 6.895 kPa
∆P = 24.7 kPa
∆P = 24.3 kPa
∆P = - ? kPa
* The raised IPE should not add significant resistance to the system. Whatever pressure drop occurs when the coolant travels up will be added back once the coolant moves back down.
^ From MY24 AWD LYRIQ. The OBCM2 is removed but a few significant bends in the added piping is expected to increase the pressure drop to make it about the same as the MY24 AWD LYRIQ.
*
Source of Pressure Drops: Magna Pressure Drop PowerPoint – Linearly interpolated from 9-12 L/min
(I don’t think I can share a copy because it is confidential? Need access to GT SharePoint)
Confidential Thermal Architecture and Pressure Drops
Notes: PUMP: Increasing flow rate, increasing pressure because increasing work,
Valve adds resistance to loop, valve decreasing pressure
-so pump increases [ressure
LTRA: Low Temperature Radiator- Crossflow heat exchanger for cooling coolant using air
Cihx

## Slide 21: System Architecture: Pressure Requirements
The HX effectively replaces the stock drive units (which are in parallel) and OBCM2. See the following slide for more detail.
Stock:
  Drive Units: ~26.9402 kPa
  OBCM2: ~17.9051 kPa
  Total: ~44.8453 kPa
This means if the added components have a pressure drop of less than 44.8 kPa, the flow should be 20 L/min.
This is not the case for the current system, which appears to have a pressure drop of about 31.4 kPa. Either the pressure needs to be under 31.4 kPa, or the current system has a larger pressure drop than 31.4 kPa due to additional bends.
Each 90 degree connector can add a pressure drop of about 0.24 kPa (see here for more detail). It is conceivable there are 10 bends which would contribute a total of 2.4 kPa of pressure drop.
Confidential Pressure Drops

## Slide 22: System Information: MY24 AWD LYRIQ
RDU
FDU
IPE
Radiator
Split Loop Direction
Rear Drive Unit
Front Drive Unit
Pump
80 W
FTPIM
RTPIM
∆P = -83.1633 kPa
∆P = 30.5537 kPa
∆P = 23.3266 kPa
Assumptions:
0% LTR
60 ⁰C
Flow
  20.4 L/min (system)
  10.1 L/min (FDU)
  10.3 L/min (RDU)
Source of Pressure Drops: GM Garbage Collector V3 https://anl.box.com/s/b6m2rktyqaqkx6ymi9irjzm4hzs1ls4f
(Need EcoCAR BOX Access)
*∆P for Radiator, IPE is not given. It is approximated as:
OBCM2
Curtesy of MAC
Chart: OBCM2 Pressure Characterization
| 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
 | 0.3 | 0.3 | 0.4 | 0.5 | 0.6 | 0.6 | 0.9 | 1.1 | 1.4 | 1.5 | 1.8
2.5969psi=17.9051kPa
Confidential Thermal Architecture and Pressure Drops
Notes: PUMP: Increasing flow rate, increasing pressure because increasing work,
Valve adds resistance to loop, valve decreasing pressure
-so pump increases [ressure
LTRA: Low Temperature Radiator- Crossflow heat exchanger for cooling coolant using air
Cihx

## Slide 23: Diagram
HX
In
In
Out
Out
S4
S1
S2
S3
1”-11 ½ NPT
To Radiator
From IPE
From EDU Loop
To EDU Loop
Pump
Reservoir
Pressure
Transducer
Pressure
Transducer
Flow Restrictor
5/8” Hose
3/4” Hose
Housing
Housing
4
2
2
1
1
3
6
5
6
5
7
8
11
12
Flow Restrictor for FEDU Loop
Flowmeter
13+15
Bleeder valve
14
Put this at high point of FEDU loop
Stock
Pump

## Slide 24: System Architecture: Proposed
FDU
IPE
Radiator
Split Loop Direction
Pump
Flowmeter
Flowmeter
80 W
HX
Flow Restrictor
Pressure Transducer
Pressure Transducer
Flowmeter
Team Pump
Coolant Reservoir
Flow Restrictor
RDU
Bleeder Valve
96 W
Confidential Thermal Architecture
Notes: PUMP: Increasing flow rate, increasing pressure because increasing work,
Valve adds resistance to loop, valve decreasing pressure
-so pump increases [ressure
LTRA: Low Temperature Radiator- Crossflow heat exchanger for cooling coolant using air
Cihx

## Slide 25: BOM
https://gtvault.sharepoint.com/:x:/s/ECE/EcoCAR/IQDrzrVUKhcvTZduIMjvDLMzAQ_aPXZBBRcs_65Yqt2Rs8o?e=LRCEgL

## Slide 26: Pressure Transducer
PX3AN2BS100PAAAX Honeywell Sensing and Productivity Solutions | Pressure Sensors, Transducers - Industrial | DigiKey
X2
$129.82

## Slide 27: Coolant Reservoir
Dorman 603-001 Dorman Coolant Reservoirs | Summit Racing
$11.99

## Slide 28: Pump
Max Flow: 20 L/min
Max Pressure:
  EDU/Flow meters –> 31.395 kPa
  Heat Exchanger -> 7 kPa
  Total -> 38.395 kPa * 1.5 FOS = 58 kPa
Bosch 039202453G Water Cooling Pump, Compact Design | Order Online
20 L/min -> 87 kPa

## Slide 29: Flow Restrictors
¾” - Four Seasons 84707 Four Seasons Heater Valves | Summit Racing
Assumptions:
  Minimum pressure drop: 2-3 kPa
  Maximum pressure drop: ∞ kPa
5/8” - Four Seasons 84706 Four Seasons Manual Shut-Off Valves | Summit Racing

## Slide 30: Slides on finding location for the HX in the vehicle were deleted since they show confidential CAD

## Slide 31: HX Location 1 and Mount
Material: 4130 Steel
Thickness: 1/8”
Loads:
  2g vertical
  5g longitudinal/lateral
Mass:
  1.2+0.11x(18 plates) = 3.18 kg
  0.054 liters x 18 channels = 0.972 liters = 0.97 kg
  Total = 4.152 kg

## Slide 32: Coolant Reservoir Mount FEA
Material: 4130 Steel
Thickness: 1/8”
Loads:
  2g vertical
  5g longitudinal/lateral
Mass of coolant reservoir:
  72oz water = 2.125kg

## Slide 33: Information Requests
General Inquiries | Alfa Laval
Call Contact Emmegi Heat Exchangers Inc. | USA
About Bell & Gossett Pumps | Contact & Support for Xylem Bell and Gossett Pump Products | Xylem US

## Slide 34: Additional Resources
OG HX dimensions bell-gossett-brazed-plate-heat-exchanger-brochure.pdf
OG HX flow and heat rejection bell-&-gossett-brazed-plate-heat-exchanger-selection-tables.pdf
HX dimensions Alfa Laval
HX Flow and heat rejection table 1 new message
HX flow and heat rejection graph WB-Series-Brazed-Plate-Oil-Coolers.pdf
  Parent: WB Series Brazed Plate Oil Coolers | Emmegi Inc.
Heat exchanger selection tool PHE Select tool | Alfa Laval